## Slide 1
2.1 Newton-Euler formulations
2.2 Lagrange-Euler formulation
2.3 Properties of Dynamic Model
2.4 Dynamics Tutorials
2.5 Neural Network Modelling
2. Robot Dynamics
- 1 -

## Slide 2
Neural Network Approximations
Neural Network Modelling of Robots
Function Approximation
Linearly Parametrized Neural Networks
Non-linearly Parametrized Neural Networks
Ge-Lee (GL) Matrix and Operator
2.5 Neural Network Modelling
- 2 -

## Slide 3
2.5 Neural Network Modelling
- 3 -
To obtain the dynamics of higher degrees of freedom manipulator as
are very simple in its representation but are very difficult, time consuming and error prone to obtain except for simple cases.
It is desirable to have generic non-linear model structures for dynamic modelling, such neural network modeling.
S. S. Ge, T. H. Lee, and C. J. Harris. Adaptive neural network control of robotic manipulators. Vol. 19. World Scientific, 1998.

## Slide 4
Square Wave Approximation
2.5 Neural Network Modelling
Here you go:

## Slide 5: Linear Approximation
A linear regression line has an equation of the form:
1. Linear regression
independent variable
dependent variable
slope of the line
intercept
2.5 Neural Network Modelling

## Slide 6: Smooth Lipschitz Function Approximation
2. Lipschitz continuous function
Approximation by Smooth Lipschitz Functions
2.5 Neural Network Modelling

## Slide 7: Neural Network Approximation
3. Universal approximation theorem
The Universal Approximation Theorem tells us that Neural Networks has a kind of universality i.e. no matter what f(x) is, there is a network that can approximately approach the result and do the job!
2.5 Neural Network Modelling

## Slide 8
2.5 Neural Network Modelling
https://ml.berkeley.edu/blog/posts/uat/

## Slide 9
Biological Neuron
A typical biological neuron is composed of:
  A cell body;
  A tubular axon: a long thin tube that splits into branches terminating in little end bulbs that almost touch the dendrites of other cells;
  A multitude of hair-like dendrites that form a very fine filamentary brush surrounding the body of the neuron;
2.5 Neural Network Modelling

## Slide 10
Synapses (from other neurons)
Axon
Nucleus
Dendrites
Cell body
Synapses (to other neurons)
Dendrites (of other neurons)
Synapses:
  Small gap between an end bulb and a dendrite.
  Basic structural and functional units that mediate the interactions between neurons.
  Can impose excitation (active) or inhibition (inactive) on the receptive neurons.
2.5 Neural Network Modelling

## Slide 11: AI Neural Networks
+1
wk1
wk2
wk3
wk4
wkm
x1
x2
x3
x4
xm
Output yk
Inputs
Synaptic weights
bk
(bias)
uk
Activation
function
dimension of input data
{ x1, x2,… xn}
number of input data
2.5 Neural Network Modelling

## Slide 12
Neural networks (NNs) consist of a large number of simple processing elements called nodes.
The nodes are interconnected by weighted links where the weights are the network’s adjustable parameters.
In control engineering, a neural network is usually used to generate input/output maps using the property that a multi-layer neural network can approximate any function, under mild assumptions, with any desired accuracy.
2.5 Neural Network Modelling
- 12 -

## Slide 13
Multi-Layer Perceptron (MLP) Network
2.5 Neural Network Modelling
- 13 -

## Slide 14
Linearly Parametrized Neural Networks: are the NNs in which the adjustable parameters appear linearly.
The output of the network
The RBF networks belong to a class of Linear Parametrized Neural Networks
Three layer neural network
2.5 Neural Network Modelling
- 14 -
The output of the hidden layer

## Slide 15
Non-linearly Parametrized Neural Networks: are the NNs in which the adjustable parameters appear nonlinearly.
2.5 Neural Network Modelling
- 15 -
General nonlinear activation function:
sigmod:
tanh:
ReLU:

## Slide 16
Non-linearly Parametrized Neural Networks
2.5 Neural Network Modelling
- 16 -

## Slide 17
2.5 Neural Network Modelling
According to Theorem, there exist ideal constants W* and V* such that
with constant for all . That is,
=
with satisfying , .
The ideal weights satisfying the above approximation are not unique. To avoid confusion, the ideal weights W* and V* are defined as

## Slide 18
GL (General-Leeway) Matrix and Operator
The output network is expressed as
Another representation is
(1)
(2)
where
2.5 Neural Network Modelling
- 18 -

## Slide 19
GL (General-Leeway) Matrix and Operator
(1)
(2)
2.5 Neural Network Modelling
- 19 -

## Slide 20
GL (General-Leeway) Matrix and Operator
Let
Define
where
2.5 Neural Network Modelling
- 20 -

## Slide 21
GL Matrix and Operator
The detailed formulations of {W} and {W}T are given by
2.5 Neural Network Modelling
- 21 -

## Slide 22
GL Matrix and Operator
where
2.5 Neural Network Modelling
- 22 -

## Slide 23
GL Matrix and Operator: Properties
The definition of transpose for GL matrix (vector) is different from that of conventional matrix (vector). It only transpose its elementary vectors locally.
The transpose of a GL row vector equals the transpose of the corresponding conventional vector. For example, .
A conventional matrix (vector) can be taken as a GL matrix (vector) by grouping the elements of the matrix (vector) into sub-vectors accordingly.
The GL product of two GL matrices (or two GL vectors) leads to a conventional matrix (or a vector). For example, and .
2.5 Neural Network Modelling
- 23 -

## Slide 24
Let a GL row vector
Def: The GL product of a square matrix and a GL row vector is defined as
2.5 Neural Network Modelling
- 24 -

## Slide 25
Note:
The GL product should be computed first in a mixed matrix product.
The GL matrix and operator will be used in the control design later.
Example:
Compute {A}•{B}C
matrix [{A}•{B}] should be computed first to get a conventional matrix [{A}•{B}].
[{A}•{B}]C is computed.
2.5 Neural Network Modelling
- 25 -

## Slide 26
Neural Network Modelling of Robots
The dynamics of a robot are function of position, velocity and acceleration, and can be described by following Lagrange-Euler equation.
2.5 Neural Network Modelling
- 26 -

## Slide 27
Neural Network Modelling of Robots
NNs have been used to approximate the complete non-linear dynamics as follows
It can be seen that the NNs are functions of , and .
Because of the difficulty in measuring acceleration for system identification and control system design, the format in the above equation has been losing ground to the NN models in which NNs are used to approximate different functions selectively for the convenience of controller design.
2.5 Neural Network Modelling
- 27 -

## Slide 28
Neural Network Modelling of Robots
The elements of D(q) and G(q), i.e. dkj(q) and gk(q) respectively are functions of q only. Thus, static neural networks (SNN), whose inputs are q only, are sufficient to model them. Suppose
where
2.5 Neural Network Modelling
- 28 -

## Slide 29
Neural Network Modelling of Robots
2.5 Neural Network Modelling
- 29 -

## Slide 30
Neural Network Modelling of Robots
2.5 Neural Network Modelling
- 30 -

## Slide 31
Neural Network Modelling of Robots
, is a function of both q and . Therefore, dynamic neural networks (DNN) of q and are necessary.
The dynamic neural network emulator of is given by
Then
2.5 Neural Network Modelling
- 31 -

## Slide 32
Neural Network Modelling of Robots
2.5 Neural Network Modelling
- 32 -

## Slide 33
Neural Network Modelling of Robots
Based on the definitions for GL matrix and operator, we have
where
2.5 Neural Network Modelling
- 33 -

## Slide 34
Neural Network Modelling of Robots
with
and
2.5 Neural Network Modelling
- 34 -

## Slide 35
Neural Network Modelling of Robots
Similarly, we have
where
2.5 Neural Network Modelling
- 35 -

## Slide 36
Neural Network Modelling of Robots
The neural network approximations of D(q) and G(q) are schematically shown in the following figure.
- 36 -
2.5 Neural Network Modelling

## Slide 37
Neural Network Modelling of Robots
Finally, the dynamic neural network model can be obtained as
Dynamic NN Model D – 1
Dynamic NN model D – 2, Static NN models can be found in chapter 4 in Reference [1]
- 37 -
2.5 Neural Network Modelling

## Slide 38
Neural Network Modelling of Task Space Dynamics
The above dynamic neural network modelling method can be directly applied to neural network modelling of robot dynamics in Cartesian space.
Corresponding to the joint space dynamics, the task space dynamics are given by
where
- 38 -
2.5 Neural Network Modelling

## Slide 39
Neural Network Modelling of Task Space Dynamics
The Cartesian space NN dynamics of robots can thus be described as
where
2.5 Neural Network Modelling
- 39 -