## Slide 1: Machine Learning for Vehicular Wireless Network and Edge Computing - Vehicular Network
Supervisor: Prof Tham Chen Khong
Name: Liu Weihao
Student ID: A0232935A
Module: EE5003
Department of Electrical & Computer Engineering
AY 21/22
Notes: Good morning professor. My name is Liu Weiaho, my EE5003 project topic is: Machine Learning for Vehicular Wireless Network and Edge Computing - Vehicular Network. Professor Tham is my supervisor.

## Slide 2: Contents
Introduction
Individual Work
  V2V communication
  Task transmission and execution
  Blockchain Based Database
Experimental results
Notes: There are 3 part in my presentation. First is the introduction. Then I will introduce my individual work in this project. Finally, I will show you the experimental results.

## Slide 3: Introduction
Notes: First, let’s start with introduction part.

## Slide 4: Background
Vehicular cloud computing
Vehicular edge computing
Blockchain-Enabled vehicular edge computing
Notes: Here are some project background. Because of the development of the intelligent transportation system, such as autonomous driving and internet of Vehicles. Then onboard computing and storage resources are not enough. So, we need to use vehicular network to increase the computing resources of the vehicles. There are two types of vehicular computing methods, vehicular cloud computing and vehicular edge computing. In this project, we use the Blockchain-Enabled vehicular edge computing.

## Slide 5: Background
Vehicular cloud computing
Vehicular edge computing
Notes: Cloud computing is a centralized system. The edge devices could access the cloud server anywhere and can send task to is via base station placed on the road. In this system, all the tasks are completed and stored by the cloud server.
Edge computing methods allow vehicles allocate the tasks to the nearby vehicles and the base station. In this system, all the tasks are completed by edge devices, but they still need a cloud server to store the global information. So, it’s a partial centralized system.

## Slide 6: Background
Vehicular edge computing
Our Blockchain dependent system
Notes: In our blockchain enabled system, we use blockchain network to replace the cloud server. All the date is stored in the block chain network.

## Slide 7: Background
Vehicular cloud computing:
  A fully centralized system
  High Network latency
Vehicular edge computing:
  Partial centralized system
  Delay in the historical data storing and fetching
Blockchain enabled vehicular edge computing:
Fully decentralized system
Similar to normal VEC, the computation happens on the edge devices. But the data is stored on blockchain nodes.
Notes: Compare these three methods.
1. Vehicular cloud computing is a fully centralized system, but because all the operations are done over the cloud, the results take time to come to the vehicle and also it is internet connectivity dependent.
2. Vehicular edge computing is partial centralized system. In VEC, the data fetching and storing delay is still there, only the computation and providing feedback delay is reduced.
In conclusion, the communication with cloud server need to take some time and increase the task delay.
3. Whereas, our blockchain enabled vehicular edge computing is a decentralized system. this methods has the benefit of reduced latency.

## Slide 8: Implementation
Scenario Creation
SUMO + OMNeT ++
Offloading Algorithm
SAC (Soft Actor-Critic )
Blockchain Network
Hyperledger – Fabric
Consensus Node Selection Algorithm
DDQN
Notes: In this project, we implemented the blockchain enabled vehicular edge computing system.
We use SUMO and omnet ++ to create a specific scenario. We generate a map contains 4 vehicles and 2 base station. Each vehicle has its own trace.
We use (SAC) Soft Actor-Critic as our offloading algorithm. Based on this algorithm, base station could select a task vehicle to execute the task.
We use Hyperledger – Fabric to set up our own blockchain network.
And we use double deep Q learning to select the blockchain consensus node.
This is our overall system flowchart. The sumo and omnet is collecting the vehicle data and storing it on mySQL local database.
SUMO program will also assign a vehicle as task vehicle every events. The assigned task vehicle will send task offloading request to base station.
Then SAC algorithm is querying the data from mysql to find out the optimal service vehicle and return this information to the vehicle.
After the training, the updated service vehicle reliability and completion ratio will be updated to the blockchain. At the same time, DDQN is also running consensus node selection algorithm based on the state of the base station, such as their CPU utilization. And select the optimal consensus node.

## Slide 9: Topology
Notes: This is our equipment topology. We have three computers as our base station. Use three raspberry Pi as our vehicle.
Actually, in the offloading part, we only use two base station, one of the computer is used to set up the blockchain network.

## Slide 10: Topology
Notes: Server 0 and 1 are our base station. One base station is running sumo,omnet, DDQN, SAC and docker engine for the blockchain and other one is running sac and docker.

## Slide 11: Individual Work
Notes: Next, I’ll introduce my individual work in this project.

## Slide 12: V2V / V2R communication
Transport layer protocol
Application layer protocol
Handling error message
Notes: First, is the communication between V2V / V2B
There are three aspects ….
3. And how to handle the error message.

## Slide 13: Transport layer protocol
Feature | TCP | UDP
Connection status | Requires a stable connection to transmit data, the conne-ction should be closed once transmission is complete | Connectionless protocol with no requirements for opening, maintaining, or terminating a connection
Speed | Slower | Faster
Latency | Higher | Lower
Broadcasting | Does not support | Support
Guaranteed delivery | Can guarantee delivery of data to the destination | Cannot guarantee delivery of data to the destination
Notes: For the transport layer protocol, there are two choices, TCP or UDP. Compare the two methods, TCP disadvantage…. But it can guarantee the delivery of the data.
Some time, we don’t know the exactly IP address of base station, UDP could send messages to the broadcast IP address. No need to build the stable connection. But UDP cannot guarantee the delivery of the data. So we need to apply some other methods to make sure the data could transmit successfully.

## Slide 14: Application layer protocol
Data retransmission
Notes: In the application layer. We apply the ACK and retransmission methods in application layer. Only when both date and ACK are received, the transmission is successful. Actually, TCP use this method in transport layer to guarantee

## Slide 15: Application Layer Protocol
Phase 1
Task generate and request phase
Phase 2
Phase 3
Phase 4
Service vehicle selection phase
Task execution phase
Results verification phase
Notes: We have four phase in the task offloading process.

## Slide 16: Application Layer Protocol
Type | Length | Head | Data1 | Data2 | Data3 | Data4 | Data5
Offloading request | 6 packets | request | Vehicle ID | Event ID |  |  | 
Results verification | 4 packets | complete | Vehicle ID | Time delay | Results | - | -
Update state | 4 packets | update | Vehicle ID |  |  | - | -
Select vehicle | 3 packets | offloading | Vehicle ID |  | - | - | -
ACK | 2 packets | ACK | Vehicle ID | - | - | - | -
Type | Length | Head | Data1 | Data2 | Data3 | Data4 | Data5
Offloading request | 6 packets | request | Vehicle ID | Event ID |  |  | 
Results verification | 4 packets | complete | Vehicle ID | Time delay | Results | - | -
Update state | 4 packets | update | Vehicle ID |  |  | - | -
Select vehicle | 3 packets | offloading | Vehicle ID |  | - | - | -
ACK | 2 packets | ACK | Vehicle ID | - | - | - | -
Notes: Here are some types our application packet and their structure.

## Slide 17: Handling error message
Error 1
While waiting for the request, other kinds of data were received.
Sol: discard the packets and back to beginning
Error 2
While waiting for the verification packet, other kinds of data were received.
Sol: discard the packets and continue to wait for the execution results
Notes: Sometimes, we will meet some errors. There are two types of errors.

## Slide 18: Task execution & transmission
Ray + UDP
HTTP + UDP
Task execution
Notes: Next, I will introduce how do we transmit execute the specific task. We used and compare two methods: Ray+UDP and HTTP+UDP

## Slide 19
A distributed compute framework
When multiple machines form a Ray cluster, each one could call the computing resources of all machines.
Ray could bind the worker node’s IP address to any custom ID. What we only need to do is pre-assigning the ID to every vehicle when they join the ray cluster.
Ray provides a “job manager” based on TCP.
Introduction of Ray
Notes: Here are some introduction of Ray

## Slide 20: Task transmission based on Ray
Step 1
Vehicle join/create a ray cluster
Step 2
Step 3
Step 4
Base stations allocate the task, and send the service vehicle ID via UDP
Task transmission & execution
Return results. ( ray.get() command)
Notes: For the task transmission based on Ray, there are four steps

## Slide 21: HTTP protocol
GET: Requests a specific resource in its entirety
HEAD: Requests a specific resource without the body content
POST: Adds content, messages, or data to a new page under an existing web resource
DELETE: The DELETE method requests that the target resource delete its state
TRACE: The TRACE method requests that the target resource transfer the received request in the response body.
OPTIONS: Shows users which HTTP methods are available for a specific URL
CONNECT: Converts the request connection to a transparent TCP/IP tunnel
PATCH: The PATCH method requests that the target resource modify its state according to the partial update defined in the representation enclosed in the request.
Notes: Next, is HTTP + UDP method. HTTP provide many methods.

## Slide 22: Task transmission based on HTTP
Step 1
Task vehicle generates the task, sends the request to the base station. (UDP)
Step 2
Step 3
Step 4
Base stations select a service vehicle and send some necessary information. (UDP)
Service sends a “GET” request (HTTP)
Service sends a “POST” request (HTTP), and send a notification (UDP)
Notes: There are also 4 steps in HTTP based protocol.

## Slide 23: Comparison
Aspects | Ray + UDP | HTTP+UDP
Transmission rate | Medium | Medium
Complexity | Simple | Complex
Communication latency | Medium | Low
Task execution time (data only) | - | 0.31 seconds
Task execution time (data and program) Execute once | 2.21 seconds | 1.32 seconds
Task execution time (data and program) Execute 50 times | 0.49 seconds | 1.32 seconds
Notes: Compare these two methods, because Ray have already configured the HTTP, it’s much simpler to use.
Data only …, data and program …
Because our task program is a python program, vehicle need some time to compile it into executable program.

## Slide 24: Parameters estimate
Task execution
Parameter | Value
 | GHz
 | Mbits
 | cycles
 | s
Parameter | Value
Notes: Next is the task execution. In SAC, it use this formula to estimate the execution time.
Cn is, Dn is … fn, available

## Slide 25: Task generate
Generate 5 task date files. 200 Kbits, 1 Mbits, 2 Mbits, 3 Mbits, 4 Mbits,
Two columns, integer data, increase from 1 to infinite (until the file size satisfies the requirements)
Select 2 random number for each columns. And generate a random
According to the pre-tested table, estimate the (Assume that the computation resources of Rpi is 7 GHz)

## Slide 26: Execution time
File size | Execution time (seconds) | Iteration times
200 Kbits | 0.02 | 1
 | 0.1 | 15
 | 0.2 | 30
1 Mbits | 0.04 | 1
 | 0.5 | 15
 | 1 | 30
2 Mbits | 0.075 | 1
 | 0.62 | 10
 | 1.3 | 20
3 Mbits | 0.1 | 1
 | 0.84 | 10
 | 1.4 | 15
4 Mbits | 0.125 | 1
 | 1.1 | 10
 | 1.55 | 15

## Slide 27: Task execution
The could change over time. (SUMO program determine the specific )
Base station send to vehicle
According to the formula, we just need to execute the original task times, the entire process could satisfy our requirements.
Estimate the time constraints
Notes: We don’t want the computation resources is a constant, we want the available computation resources could change over time.

## Slide 28: Blockchain Based Database
Introduction
Configuration
Smart contract
Notes: Then I’ll will introduce our blockchain based database

## Slide 29: Structure – Hyperledger Fabric
Level 1
Entire Blockchain network
Level 2
Peer Nodes
Level 3
Organization
Notes: We use Hyperledger Fabric to set up our own blockchain network
There are 3 layer.

## Slide 30: Key concepts
Ledger:
  Distribute database
Channel:
  Connect the peer node and the ledger.
Chaincode
  Smart contract
Consensus Node
  Approve the transaction.
Notes: Next, there are some key concepts in our blockchain network

## Slide 31: Ledger
World state:
  A database that holds current values
Blockchain:
  A log of transactions grouped in blocks. History information
Block:
  Specific transaction data
Notes: Th ledger contains two part.

## Slide 32: Fabric Configuration
Step one: Set up the blockchain network
  Set up Certificate Authority (CA)
  Create identities and MSPs
  Deploy peers and ordering nodes
Step two: Set up docker environment
  Bind the ID address of other nodes
Step three: Ledger config
  Create / join a channel
  Install the smart contract (chaincode)
Notes: Then is the fabric configuration. We need to make sure our blockchain network could work properly.

## Slide 33: Smart contract
Vehicle:
  History recording of the vehicles
Task:
  Task information
SACC:
  Base station current state
Notes: Smart contract just like a table in the traditional database. User could use smart contract to access the corresponding table, and update & query the data.
We have 3 smart contract in our project.

## Slide 34: Comparison
Comparison of different database
Notes: Then compare the blockchain based database with some centralized database.
It only needs to spend 0.3s to upload the data to the database. Besides, it also supports multiple users edit the same data at the same time because of its consequences algorithm.

## Slide 35: Experimental results
Notes: Finally, is our experimental results.

## Slide 36: Scenario
Notes: This is the simulation we have used to collect the vehicle data. Where vehicles are moving continuously and sharing the information with the RSUs.

## Slide 37: Simulation

## Slide 38: THANK YOU